## Slide 1: Uncertainty Quantification for Cyber-Physical Pressurized Water Reactor Experiments
Dr. Taylor K. McKenzie (PI)
Co-authors: Dr. Christopher Lamb, Dr. Thomas D. Tarman
Notes: Hi and thanks for joining! I’m Taylor McKenzie and today I’ll be discussing this study into Uncertainty Quantification for Cyber-Physical Pressurized Water Reactor Experiments.

## Slide 2: Introduction
Ph.D. in Economics from University of Oregon in 2017
  Studied Industrial Organization, choice modeling, empirical models of competition
  Dissertation identified changes in pricing, competition, and technological change in US freight rail industry following deregulation
Joined Sandia National Laboratories in 2017
  Cyber risk and resilience analysis: Statistical analysis and uncertainty quantification to measure risk to/resilience of cyber-physical systems using emulation and experimentation
  Interagency Nuclear Safety Review Board: Risk analyses of launches of spacecraft containing nuclear material, including Mars 2020/Perseverance
  Strategic Futures and Policy Analysis: Telecommuting/hybrid work posture, COVID-19 economic impact analyses, Global Futures studies on Economic Value & National Security and Knowledge Management
Notes: Before kicking off, I’ll give just a brief introduction and some context for where this research fits.
I received my Ph.D. in Economics from the University of Oregon in 2017, where I studied industrial organization and focused on choice modeling and empirical models of competition. My dissertation focused on identifying changes in pricing, competition, and technological change in the US freight rail industry following its partial deregulation.
I joined Sandia National Laboratories in 2017, and I started in a group doing Cyber Resilience R&D. While I was in that role, I contributed to and conducted analysis looking at risk and resilience of cyber systems, and specifically performing statistical analyses and uncertainty quantification that enabled using cyber emulation and experimentation to measure risk and resilience. This is where the research I’ll be discussing mostly fits in.
During that time, I also joined the Interagency Nuclear Safety Review Board, which performs risk analyses of launches of spacecraft containing nuclear material. Through 2019, our work was focused on Mars 2020 and the Perseverance rover, which landed on Mars in 2020, and since then have been preparing for analysis of a nuclear thermal propulsion mission, which is starting up this year.
Then in early 2020 I joined the Strategic Futures and Policy Analysis group here at Sandia. I actually shifted roles one week before lockdown, so was able to jump right in into some policy studies looking at Telecommuting that ultimately shaped Sandia’s hybrid work posture and economic impact analyses that supported Sandia’s COVID modeling effort. And, amongst other research, I’ve been involved with Sandia’s Global Futures series, which considers domains and areas where there could be disruptions over the next 10-20 years that would have major implications for Sandia strategy and national security as a whole. In particular, I was one of the PIs on the Future of Economic Value and National Security and am the lead PI the current study on the Future of Knowledge Management.

## Slide 3: Agenda
Uncertainty quantification for cyber-physical pressurized water reactor experiments (McKenzie et al. 2020) [1]
  Background and system description
  Research problem and uncertainty quantification approach
  Kernel smoothing and Gaussian process approaches
  Results
  Discussion and impacts
Notes: To give you an idea of what we have planned: Again, I’ll be discussing this paper, “Uncertainty quantification for cyber-physical pressurized water reactor experiments”, which was presented at the International Conference on Nuclear Engineering in 2020. I really enjoy talking about this research because there’s a good story to tell about the research process, some good lessons learned about not taking assumptions for granted, and I think is a good look into what cyber emulation and experimentation is about and how uncertainty quantification is often an integral part of that process.
So I’ll start off with a bit of background into this research and application area, broadly what cyber emulation is, and I’ll also cover some of the important details of pressurized water reactor systems.
I’ll then talk through our specific research problem and why uncertainty quantification is needed and broadly what uncertainty quantification is aiming to do.
Next, I’ll go into a couple of specific uncertainty quantification approaches we considered for this application. I’ll discuss kernel smoothing, which was initially promising but ended up being a failed approach, at least in its standard form, due to some peculiarities of the data we’ll discuss. I’ll also discuss Gaussian processes, which are functionally similar to kernel smoothing but have some unique advantages for this particular application, and are what we ultimately opted for in this particular case.
I’ll then talk through some of our results and finish with a discussion on extensions and improvements as well as the impacts this work had.

## Slide 4: Background and System Description

## Slide 5: Background
Sandia has significant capabilities in cyber-physical emulation environments
  The SCEPTRE platform was developed to “analyze how cyber-initiated events affect the physical world,” using a network emulation with hardware-in-the-loop capabilities to model, test, and validate cyber-physical systems [2]
  Used to assess risk and resilience of cyber-physical systems to natural and adversarial disruptions. Systems studied include critical infrastructures (e.g., power, oil/gas, chemical), space/satellite systems, industrial control systems (ICSs).
This project was funded by sponsors from DOE-NE, who were interested in the risk posed to cyber-physical nuclear power generation
  Specifically interested in metrics to evaluate risk of catastrophic outcomes given a particular attack scenario
Cyber-physical emulation is particularly well-suited for this analysis
  Nuclear reactor mechanics/dynamics are well understood and high-fidelity simulation models exist for these systems
  Cyber risk to nuclear reactor systems is less understood and more difficult to simulate with needed fidelity
Notes: So to start off, Sandia has developed significant capabilities into cyber-physical emulation environments. I’ll talk through this bit on broadly what the goals of these capabilities are, and will talk more about how we define emulation in the next slide. In particular, the SCEPTRE platform was developed at Sandia to “analyze how cyber-initiated events affect the physical world,” using a combination of network emulation and hardware-in-the-loop capabilities to model, test, and validate cyber-physical systems. SCEPTRE has been used to assess risk and resilience of cyber-physical systems to a range of both natural and adversarial disruptions, with systems including various critical infrastructures like power, oil and gas, and chemical facilities, space and satellite systems, and industrial control systems in general.
This project was funded by sponsors from DOE-NE, and they were interested, broadly, in assessing risk posed to cyber-physical nuclear power generation. In particular, they were looking for ways to measure risk of catastrophic outcomes given a particular attack or disruption scenario.
And again, I’ll talk more about what emulation is in the next slide, but as it turns out, cyber-physical emulation is a good choice for this analysis. In particular, nuclear reactor mechanics and dynamics are well understood and computer simulations are a great approximation to the actual systems. On the other hand, cyber risk, and in particular how cyber events propagate to and interface with physical events, is less understood. So, we rely on emulating cyber components and using, for example, real software and network protocols (Modbus).

## Slide 6: Emulation and Cyber Experiments
We want to evaluate how a critical system would respond to a given disruption
  Quantify impacts
  Identify and quantify effectiveness of mitigation strategies
Affecting operations of a critical system is infeasible
  Emulation provides ability to create a sufficient representation of a system, including hardware in the loop
  Emulation can be used to see how actual system would respond without affecting operations
Parameters of the system, emulation, or disruption may be uncertain
  Thus, outcomes are also uncertain and can be described by a probability distribution
  Uncertainty quantification (UQ) involves propagating input uncertainty to determine/approximate the distribution of outcomes
Notes: So, in research that draws on emulation, we’re wanting to evaluate how a critical system would respond to a given disruption. And we’re doing this to both quantify impacts of a disruption as well as identify and quantify the effectiveness of potential mitigation strategies.
Now with most or all critical systems, doing anything that might affect the operations of the actual system is not an option. So, we need to rely on some model of the system to give us an idea of what impacts might look like.
Turning to the graphic on the bottom of the slide, what emulation is trying to do is bridge this gap between the actual system and a fully abstracted representation of that system. Emulations will use abstract representations of components for which simulations are adequate or where things like scale or cost make using an actual version of that component infeasible. So, in practice, we frequently simulate (use an abstract representation of) hardware, physical processes and physical system dynamics, things like power system models and reactor dynamics. Then, for components for which there’s not a great simulation, we use actual representations for those components. These frequently include software components and the protocols that pieces of the system use to communicate with each other. And finally, there’s an interface between the abstract hardware and real software that completes the representation of the system as a whole.
So, emulation providing this ability to create a sufficient model of the system, allowing to simulate using representations where it makes sense and its convenient, and use real representations in other cases where we need that fidelity. And those real representations can be anything from actual software and protocols to real hardware that we can plug into the loop. Overall, this gives us the ability to create a model that’s as high-fidelity as is feasible and makes sense that enables us to have a good view into how the actual system would respond.
The issue is, a model is just that, and parameters of the system, emulation, or disruption may be uncertain. And therefore outcomes are also uncertain and are described by an unknown probability distribution. Uncertainty quantification, or UQ, in its most general form involves propagating uncertainty in inputs to determine or approximate the distribution of outcomes.

## Slide 7: Proof of Concept System: Pressurized Water Reactor
Image sources: NRC, Wikipedia
Notes: Before really diving into the research problem, let’s talk more about pressurized water reactors, or PWRs. PWRs are a very common nuclear reactor design, accounting for about 65% of nuclear power generation in the United States in 2021. This graphic comes from the Nuclear Regulatory Commission and shows a general PWR design.
What makes PWRs unique is a dual coolant loop design. In the figure, you’ll see a red/orange/yellow loop which is called the primary loop, and a blue loop that includes the steam generator, turbine, and condenser which is called the secondary loop. In the primary loop, coolant (which is most commonly water) is used to moderate nuclear reactions occurring in the reactor and cool the reactor. As coolant in the primary loop is circulated, it heats coolant in the secondary, which produces steam that drives a turbine and is then recondensed back into water. Now, this dual loop design is convenient because it only requires significant radioactive containment coolant in the primary and, notably, not the coolant that’s driving the turbine. Also, what’s called “heavy water” may be used in the primary because it’s an exceptional moderator of nuclear reactions, but is much more expensive than “regular” water and isn’t necessarily what you want to use to drive a turbine, for example.
Now, the primary loop is pressurized to allow the coolant to reach much higher temperatures without turning to gas. In general, coolant turning to gas unexpectedly (“flashing to steam”) can be catastrophic because that can lead to large, unpredictable swings in pressure that can damage pipes, vessels, and other components. For context, the primary is typically kept at a temperature of about 345C and a pressure of 15-16 Mpa (just below the triple point of water).

## Slide 8: Proof of Concept System: Pressurized Water Reactor
Image sources: NRC, Wikipedia
Notes: To maintain pressure in the primary loop, a pressurizer sits on top of the primary and is the only component of the primary loop that does (should) contain gas. Pressure of the entire loop is controlled by changing pressure of gas in the pressurizer. There are electric variable heaters that increase the heat and pressure of the pressurizer, and there are sprayers that spray relatively cool water in the pressurizer and reduce temperature and pressure.
So, as you might imagine, the pressurizer is a critical component of the primary loop and overall PWR system. If pressure is allowed to get too low, water could flash to steam and damage pipes, vessels, and other components. If pressure gets too high, components of the system could also be damaged, albeit probably in a less dramatic way but catastrophic nonetheless.
Before moving on, are there any questions about PWR systems in general?

## Slide 9: Proof of Concept System: Pressurized Water Reactor
Pressurized water reactors (PWRs) are a nuclear reactor design with the following characteristics:
  Two coolant loops:
    Primary loop where coolant cools and moderates the reactor
    Secondary loop where coolant is heated by the primary and generates steam that drives turbines
  Pressurized primary loop, which allows coolant to reach high temperatures while remaining liquid
    Typical pressure: ~15-16 MPa
    Typical temperature: ~345 °C
In a dual coolant loop design, only coolant in the primary loop requires significant radioactive containment
Pressurizer sits on the primary coolant loop and maintains appropriate pressure
  Too low could allow water to flash to steam. Too high could damage vessels/pipes/components.
  Electric heaters increase temperature/pressure, water sprayers reduce temperature/pressure
Pressurizer is a critical component of the system, and failures are highly consequential
Dual loop design is unique to PWRs, motivating risk analysis specific to PWRs
  PWRs are a very common design, accounting for 65% of nuclear power generation in the U.S. in 2021 [3]
Notes: This slide is just writing out what I said in words in the last couple slides, just here for your reference.

## Slide 10: Proof of Concept System: Cyber-Physical PWR System
We draw on a cyber-physical emulation of a PWR system
Abstract hardware: Pressurizer (including electric variable heaters and spray valves to control pressure) described by numerical model implemented in Simulink
Real software: Supervisory control and data acquisition (SCADA) system, including server, router, network switches, remote terminal units (RTUs) to interface with pressure sensors, and programmable logic controllers (PLCs) to actuate heaters/sprayers
Notes: SCADA system includes virtualized hardware components, but those components are speaking to each other/using the same protocols as real components
So the in last couple slides, we talked through the physical PWR system, but of course we’re working with a cyber-physical PWR system; that is, one that includes some cyber components to observe and control physical processes. This slide shows a representation of the cyber network we built and used.
Again, we’re leveraging an emulation, which aims to make most hardware components abstract through simulation and uses real representations of software components. The hardware we’re abstracting is the pressurizer, which is described by a numerical model implemented in Simulink and, of course, includes electric variable heaters and spray valves to control pressure. On the other side, we’re using real versions of the supervisory control and data acquisition, or SCADA, network, which includes a server, router, network switches, remote terminal units, or RTUs, to interface with pressure sensors, and programmable logic controllers, or PLCs, to actuate the heaters or sprayers.

## Slide 11: Research Problem and Uncertainty Quantification Approach

## Slide 12: Research Problem
In general, previous risk/resilience analyses, red team assessments, and intelligence can be used to form a distribution of disruptions
  For this analysis, attacks will continually inject a specified control value to the pressurizer heater and/or sprayer. The injected values and which component(s) are targeted are assumed to be random.
Given a distribution of attacks, our goal is to estimate the probability that a catastrophic outcome will occur
  Severe consequences can occur if differential pressure on the pressurizer exceeds 1 MPa
  Emulation is computationally expensive, making simple Monte Carlo analysis infeasible
  Need to use methods that can accommodate limited numbers of observations while correctly express uncertainty
Uncertainty quantification (UQ) methods can be used to estimate outcomes and evaluate uncertainty in those estimates when obtaining additional observations is costly

## Slide 13: Disruption and Quantities of Interest
Disruption:
  An attacker is assumed to have gained access to the SCADA network and is able to override control values being fed to the heater and/or sprayer
  The SCADA network is assumed to not have any intrusion detection or prevention system
  The attacker is assumed to target either heater, sprayer, or both, each with probability 1/3
  The attacker continuously injects malicious values to targeted actuator(s) for two minutes. Injected values are constant over the attack and are assumed to be uniformly distributed over [0, 100].
Notes: For the disruption, we assume an attacker has exploited a vulnerability in the system and targets either the heater actuator, sprayer actuators, or both actuators, each with probability 1/3. The attacker will then continuously inject false values to the targeted actuators for two minutes. The injected values are constant over the course of the attack and are distributed uniformly on the range from zero to 100.
Thus, the inputs to the emulation are which actuator is targeted and what values are injected to the targeted actuators.
Next, severe consequences can occur if differential pressure of the heater or sprayer exceeds one mega-Pascal.
We focus on estimating the probability that differential pressure will exceed one mega-Pascal at any point during the two minute attack, conditional on which actuator is targeted and values injected to the targeted actuators.
Inputs used to fit the Gaussian process were generated with Latin hypercube sampling, the emulation was run with those inputs, and outcomes were recorded to use in fitting the Gaussian process.
The standard Gaussian process model, which ordinarily describes real-valued outcomes, was adapted to describe binary outcomes. The Gaussian process was fit using the Stan platform, using 1000 warmup iterations and 1000 sampling iterations.

## Slide 14: UQ vs. Statistics
UQ methods were originally developed to serve as a proxy for deterministic computer simulations
  Sandia has a history of developing UQ methods and tools for simulations of nuclear weapons systems
  Simulations historically required major computing infrastructure and could only be feasibly evaluated a small number of times. However, analyses of those systems/simulations required many observations/evaluations.
UQ aims to describe the distribution of outcomes given uncertain parameters/inputs when observations are limited and/or generating new observations is costly
How this is different than statistics:
  Statistics often focuses on estimating the relationship between inputs and outputs. UQ focuses on the relationship between input uncertainty and output uncertainty.
  UQ applications utilize more machine learning (ML) methods (explainability is not necessarily a focus)
  In many UQ applications, the researcher is able to generate new data at a cost
There are a few approaches UQ analyses typically take
  In the upcoming slides
    are inputs, are outcomes
    are random variables, are specific values/realizations

## Slide 15: UQ Applications (1)
Approach 1: Given a distribution of inputs , describe the distribution of outcomes
Common approach: Obtain a function such that
Since the distribution of is the sole focus, need not describe any relationship that may exist between and
Polynomial chaos expansions are frequently employed in this application
  takes the form of an th order polynomial
  New observations of can be generated in a way that minimizes expected distance between distributions of and
  Useful as a proxy in Monte Carlo simulations when exact relationship between and is not important

## Slide 16: UQ Applications (1)
Approach 1: Given a distribution of inputs , describe the distribution of outcomes
Common approach: Obtain a function such that
Since the distribution of is the sole focus, need not describe any relationship that may exist between and
Polynomial chaos expansions are frequently employed in this application
  takes the form of an th order polynomial
  New observations of can be generated in a way that minimizes expected distance between distributions of and
  Useful as a proxy in Monte Carlo simulations when exact relationship between and is not important

## Slide 17: UQ Applications (2)
Approach 2: Given a value of inputs , predict the deterministic outcome
There is some function such that conditional outcomes are described by
Want to construct an estimate such that
  for all observed
  for all
  Ideally, approximately follows a known distribution (e.g., )
Interpolation and similar methods are popular: Splines, Gaussian processes, sometimes other ML methods
  Observed points are fit exactly, points between are estimated with a smooth curve
Useful as a proxy in simulations when exact relationship between and is important

## Slide 18: UQ Applications (3)
Approach 3: Given a value of inputs , describe the distribution of the non-deterministic outcome
There is some function such that the conditional distribution of outcomes is described by
  describes uncertainty in and uncertainty in the relationship between and
Want to find such that for all
In practice, assumptions about distribution family and continuity/smoothness are made
Useful for when outcomes are not deterministic and when the relationship between and is important

## Slide 19: Research Objective and General Approach
Goal: Given a distribution of attacks, estimate the probability that differential pressure on the pressurizer will exceed 1 MPa
  It would also be useful to identify attack scenarios in which risk is high and estimate distributions of outcomes under particular attack scenarios
Approach 3 (estimate distribution of given any value for ) provides insights into both overall risk and the relationship between attack characteristics and impacts
It is not apparent ex ante whether the relationship between inputs and outcomes are simple/monotonic/etc.
  Approach needs to be flexible (e.g., smoothing) and needs to provide conditional distributions of outcomes
Notes: Use this slide to explain why goal 3 is appropriate. Need to explain why it’s useful to have a continuum of distributions for this application.
Could also explain why GPs here…
Sneak peek into data could be useful here… Understand that inputs are distribution of values attacker is injecting to heater/sprayer and outcome is (uncertain) event that differential pressure exceeds 1 MPa given those value.
Goal 3 allows for identification of relationships between values injected and probability of consequence as well as overall understanding of probability of consequence.
Outcome is binary, and it’s not clear whether there is a simple/linear/monotonic relationship with outcome/odds. So, need some kind of nonlinear data-driven model; something like kernel smoothers are one appropriate approach.

## Slide 20: Kernel Smoothing and Gaussian Process Approaches

## Slide 21: A Failed Approach and Lessons Learned
Kernel smoothing was initially selected to analyze data
  Fits a smooth curve through noisy data; researcher specifies/selects “kernel” which controls level of smoothing
  Predictions of conditional outcomes are asymptotically normal, providing conditional distribution of outcomes
    Result relies on assumptions similar to Central Limit Theorem (i.e., defined mean, finite variance)
  Constrained kernel smoothing can implement inequality constraints to accommodate binary outcomes, ensure predictions are in
However, the following issues arose:
  Asymptotic distributions for constrained kernel smoothing are often not straightforward, involve additional distributional assumptions [4]
  Other real-valued outcomes from this emulation did not meet assumptions necessary for asymptotic distributions to be valid
    E.g., log-time-to-threshold outcomes often showed evidence of infinite variance
Needed an alternative approach that didn’t rely on asymptotics and could produce conditional outcome distributions for binary outcomes in a more direct way

## Slide 22: Gaussian Processes
Gaussian processes (GPs) are functionally similar to kernel smoothing
  Similar objective: Fit a smooth curve through noisy observations
  Major difference: Gaussian processes are likelihood-based, whereas kernel smoothers are not
    Enables formal inference for smooth curve estimates without relying on asymptotics, at the cost of needing to specify a generating distribution
Standard GP form:
  : Inputs, parameters to emulation
  : Outcomes of emulation, conditional on
  : Function mapping inputs to outcomes
  : Kernel function describing degree and form of smoothing
  : Parameters of the GP to be fit
  Identity matrix with size equal to the number of observations used to fit the GP
GP details
Notes: Need some motivation somewhere (maybe not here) for using Bayesian/simulation methods. Difficulty of propagating uncertainty in parameter estimates to uncertainty in predictions. Parameter instability issues in generalized GPs like Bernoulli models (esp. applicable here). Assumptions for asymptotics are not necessarily met, issues with doing asymptotics with Bernoulli outcome.

## Slide 23: Gaussian Processes vs. Kernel Smoothers
Standard GP form:
A few comments and comparisons with kernel smoothers:
  Eq. (1) is a distribution over functions. In estimation this describes observed data, but extends to all in the range of . So, sampling methods will generate draws of entire functions.
  is the “kernel” and plays a similar role as in kernel smoothers: Control how much smoothing occurs and fine-tune shape of estimated curves.
  Many parameters are sampled/evaluated in (1) (# of observations), so the convolution is frequently used.
    Lose the ability to directly evaluate functions/predicted values, but the distribution of function values for observed and hypothetical data can be inferred
    Convolution isn’t always possible/straightforward if eq. (2) is not a normal sampling statement; e.g., binary outcomes
(1)
(2)
GP details

## Slide 24: Gaussian Process for Binary Outcomes
The standard GP formulation assumes outcomes are real-valued, normally-distributed
  Not appropriate for modeling binary outcomes
GP can be extended to binary outcomes through use of a link function (denoted )
A popular choice for is the inverse logit function:
To review, the binary outcome GP formulation:
  Fits a smooth curve through noisy data very similarly to kernel smoothing
  Does not rely on potentially invalid normality assumptions since focus is on a binary outcome
  Enables straightforward inference that leverages likelihoods explicitly specified by the model, even for constrained outcomes

## Slide 25: Sampling Procedure
Inputs: Which actuator is targeted, what value(s) are injected to targeted actuator(s)
Emulated PWR System
Heater Actuator
Sprayer Actuator
Outputs: Indicator of whether differential pressure exceeded 1 MPa at any point during the attack
We focus on estimating probability that differential pressure will exceed 1 MPa at any point in the two minute attack, conditional on which actuator is targeted and values injected to targeted actuator(s)
Input samples used to fit the GP were generated with Latin hypercube sampling
  Generates a sample of inputs that effectively spans the input space
  Sample contained 250 attack scenarios: 83 targeted heater, 83 targeted sprayer, and 84 targeted both
Emulation was run with each input value and outcomes were recorded
  Emulation initialized then allowed to stabilize for 5 minutes, followed by a 2 minute attack
  Obtaining additional observations is relatively time-intensive

## Slide 26: Estimation Issues and Procedure
Potential estimation issue: Binary outcome models can suffer from parameter instability, especially when using more flexible relationships between inputs and outcomes [5]
  Can cause convergence issues for classical statistics estimation methods
  Bayesian statistics estimation methods offer a solution
    Must specify priors over parameters
    Convergence can be assessed more reliably (e.g., trace plots/diagnostics)
Following Gelman et al. [6], half-Cauchy priors were assumed for kernel parameters
Model was estimated using No U-Turn Sampling as implemented in the Stan platform [7]
  Sampler used 1000 burn-in and 1000 sampling iterations
  Trace plots/diagnostics were used to assess convergence of Markov chain
for

## Slide 27: Results

## Slide 28: Conditional Probability Estimates
Probability of reaching 1 MPa threshold when only the heater actuator is targeted, conditional on values injected to heater actuator
Probability of reaching 1 MPa threshold when only the sprayer actuator is targeted, conditional on values injected to sprayer actuator
Probability of reaching 1 MPa threshold when both actuators are targeted, conditional on values injected to both actuators
Notes: Next, we move to results. First, conditional probability estimates are shown on this slide. The left figure shows the probability of crossing the one mega-Pascal threshold if only the heater is targeted, middle shows if only sprayer is targeted, and right shows if both actuators are targeted. These figures begin to show some system behavior and avenues for possible mitigations. For example, it does not appear that the heater actuator plays a significant role, and the probability of crossing the threshold rises dramatically above sprayer values of about 40.
Bumps in the middle and right figure are due to iterations that did not result in crossing the one mega-Pascal threshold. These would indicate some overfitting, and we will discuss some ways to address in a couple slides.

## Slide 29: Overall Probability Estimates
Fitted GP used to estimate overall probability of crossing 1 MPa threshold
  Heater actuator, sprayer actuator, and both actuators targeted with 1/3 probability each
  Values injected to targeted actuator(s) uniformly distributed on [0, 100]
GP surrogate function provides computationally feasible method of approximating these probabilities
  Each iteration of the emulation takes 5 minutes to set up/stabilize + 2 minutes for attack
  Each sample of the GP takes ~0.7 seconds (3.5 GHz processor)
Notes: We can also use the fitted Gaussian process surrogate function to estimate the overall probability of cross the one mega-Pascal threshold. Recall that the heater actuator, sprayer actuator, and both actuators are each targeted with probability 1/3, and values injected to targeted actuators are uniformly distributed on the interval from 0 to 100. The event tree and results are shown in the figure on the right. Overall, given assumptions about the attack, we estimate there is a 35.7% probability the threshold will be crossed given the attack occurs.
Using a Gaussian process surrogate function makes it computationally feasible to approximate these probabilities. To illustrate, each iteration of the emulation takes five minutes to set up and stabilize and an additional two minutes for the attack.
On the other hand, each sample of the Gaussian process takes about 0.7 seconds.

## Slide 30: Discussion and Impacts

## Slide 31: Methodological Extensions
Investigation of analytical methods other than GPs
  Constrained kernel smoothing + bootstrapping for binary outcomes
Alternative forms of GP model
  Problem: Results show some evidence of overfitting
    Indicates that estimate uncertainty may be under-quantified, increasing bias in estimates
  Potential solutions:
    Adaptive sampling to focus on regions where overfitting appears to have occurred
    Impose constraints such as monotonicity where justified
    Alternative priors to “force” greater prediction uncertainty (last resort)
Alternative sampling methodologies to boost overall UQ/GP efficiency
Extension to real-valued outcomes
  Problem: Fat-tailed distributions for some real-valued outcomes complicate asymptotics
  Requires more explicit modeling of outcome distributions, which can be more difficult to work with computationally/numerically
Notes: While this research illustrates one method to perform uncertainty quantification on a cyber experiment with noisy outcomes, there are several extensions that could be pursued.
First, this research only considers a Gaussian process surrogate function. There are many other choices of surrogate functions available that one could compare with, for example, goodness-of-fit metrics.
There are also alternative forms of the Gaussian process model that could be considered. Additional constraints like monotonicity could be imposed, and alternative correlation structures could be explored.
While this research used Latin hypercube sampling to generate data to fit the surrogate function, other sampling methodologies could yield greater efficiency.
Finally, this research focused on a binary outcome but could also be used to describe real-valued outcomes. Our preliminary results indicate some outcomes may be distinctly non-normal (such as Cauchy distribution), so standard methods may need to be adjusted to be applicable.

## Slide 32: Impacts
Lessons learned and informing UQ cyber emulation analyses for other applications
  Assumptions supporting asymptotics may not be valid for real-valued outcomes. Methods that avoid asymptotics are preferable (possibly necessary). Candidates include Gaussian processes and bootstrapping.
  Reframing outcomes can be useful to avoid difficult distributional assumptions and simplify analysis
    E.g., can real-valued outcomes be transformed into binary/categorical indicators and still capture important information?
This proof-of-concept model was extended to be more representative of actual PWR systems, directly useful to DOE-NE sponsor
  Consider intrusion detection/prevention systems on SCADA network
  Utilize previous threat/vulnerability analyses and intelligence to develop more sophisticated/realistic distribution of attacks

## Slide 33: Acknowledgements
Thanks to Eric Vugrin, Robert Bruneau, Meg Galiardi, Amanda Gonzales, Jamie Thorpe, Ray Fasano, Tim Ortiz, and Ryan Kao
Work made possible by funding from DOE-NE Cyber Security for Nuclear Facilities
Notes: We would like to thank Eric Vugrin and Robert for their leadership and thoughtful suggestions, Meg Galiardi, Amanda Gonzales, and Jamie Thorpe for their help with our UQ experiments, Ray Fasano for the PWR Simulink model and model description, and Tim Ortiz and Ryan Kao for the minimega model of the cyber system.
Finally, this work was made possible by funding from DOE-NE Cyber Security for Nuclear Facilities.

## Slide 34: References
[1] McKenzie, T., Tarman, T., and Lamb, C., 2020. “Uncertainty quantification for cyber-physical PWR experiments”. Proceedings of the 28th Annual International Conference on Nuclear Engineering.
[2] Sandia National Laboratories, 2019. SCEPTRE: SCADA as a Platform.
[3] Nuclear Energy Institute, 2022. U.S. Nuclear Operating Plant Basic Information.
[4] Cai, T., Low, M., and Xia, Y., 2013. “Adaptive confidence intervals for regression functions under shape constraints”. The Annals of Statistics, 41(2), pp. 722-750.
[5] Allison, P., 2009. “Fixed effects regression models”. SAGE Publications.
[6] Gelman, A., et al., 2006. “Prior distributions for variance parameters in hierarchical models (comment on article by Browne and Draper)”. Bayesian Analysis, 1(3), pp. 515-534.
[7] Stan Development Team, 2018. “RStan: The R interface to Stan”. R package version 2.18.2.

## Slide 35: Comments/Questions

## Slide 36: Backup Slides

## Slide 37: Gaussian Process Details
Main model:
Inference:
Dimension reduction using convolution:
(1) + (2)
(1)
(2)
Return to main presentation